A few approaches to firmware projects design

---
Boards set for Raspberry Pi extension.
- No compiler/toolchain needed for making the system work.
- Python based computer side SDK.
- Pawn embedded scripting machine.
- Boards in stack are driven by either main board, PC or Raspberry Pi.
- If coupled with Raspberry can provide it with power when needed.

---
Boards set for Raspberry Pi extension.

---
Boards set for Raspberry Pi extension.
Two extension boards with motor drivers, PWM, IO pin arrays.
Main board with adjustable Buck, Boost converters, and standard periphs (USART, SPI, I2C, USB) exposed at edge connectors.

---
Boards set for Raspberry Pi extension.
Python and Pawn scripts examples side by side.
New embedded script flashing dialog.

---
Scalable controller for pneumatic mechanism.
- The goal was to design cheap controller for a few mechanisms driven by pneumatic valves and electric motors.
- Minimize parts cost and PCB tooling cost.
- Number of controllers was small.
- Number of elements to control was not fixed and was relatively large ~150-200.

---
Scalable controller for pneumatic mechanism.
Taking into account all possible combinations of pneumatic actuators, motors and sensors in all mechanism configurations
- it turned out that “optimal” numbers of different PCB types was 2.
- Boards are interconnected by power lines, common I2C bus and 2 digital lines for synchronous triggering.
- External communication was performed via either I2C or USB by single board computer running Linux OS.
- During debugging stage it also was equipped with embedded Pawn machine for easy movement algorithms trying/implementing.

---
USB powered expandable motor controller
- The goal to minimize development resources and unify board design to maximum number of aplications.
- The same scalable approach was applied.
- PCB with integrated USB driven power supply. Power supply part may be cut off for on top mounting or left blank for bottom mounting, see picture.
- One board can drive 2 stepper motors, 1 DC motor, 2 sensors.
- Scalable design by reusing the same board a few times and addressing individual boards using I2C bus and GPIO triggering for synchronization.

---
3rd party bipotentiostat control module.
- Objective was to simultaneously spend minimum resources as client had no extra money to finance the development but achieve challenging requirements.
- Analog precision to achieve ~1mV
- 2 analog outputs +/-10V
- 4 analog inputs +/-10V
- External digital trigger
- One switchable analog output
- USB computer interface
- ~1000 points (4 readings per point) per second, 10V per second sweep rate.
- Parameters of hardware to be controlled were unknown.

---
3rd party bipotentiostat control module.
- Mostly used 5% or 1% resistors
- Built in mcp3063 based boost 5V to 12V and inverting 5V to -12V switching sources.
- On board temperature sensor for calibration purposes.
Calibration setup was equipped with potentiometers and a heater under near the device for statistical data acquisition.

---
3rd party bipotentiostat control module.
- Input filter design and Bode plot.
- Based on Chebyshev filter but with lowered response near cutoff requency to reduce oscillations caused by step response.

---
3rd party bipotentiostat control module.
Examples of parameters and outputs cross correlations
- After gaining statistical data went to higher dimensional space by involving first few powers of each parameter, exponentiation and a few parameter products.
- Used this data set to find the best mean out of sample error by applying linear regression to all possible parameter combinations.
- Obtained formulas and dropped parameters which didn't improve match better then chosen margin ( )
10^{-5}

---
3rd party bipotentiostat control module.
Formulas obtained for data readings conversion
V_{out} = a_{1} * dac_{1} + a_{2} * dac_{2} + a_{3} * dac_{1} * T + a_{4} * dac_{ 2 } * T + a_{5}*T^{3} + a_{ 6 }
V_{i n} = a_{1} * adc + a_{2} * T + a_{3} * T^{2} + a_{4} * T^{3} + a_{5}

---
3rd party bipotentiostat control module.
PC based software for driving control module.
Just nice looking electrochemical cycling I(V) curve obtained during system testing.