A few approaches to firmware projects design

---
Boards set for Raspberry Pi extension.
- Python based computer side SDK.
- Pawn embedded scripting machine.
- Boards in stack are driven by either main board, PC or Raspberry Pi.
- If coupled with Raspberry can provide it with power when needed.

---
Boards set for Raspberry Pi extension.

---
Boards set for Raspberry Pi extension.
Two extension boards with motor drivers, PWM, IO pin arrays.
Main board with adjustable Puck, Boost converters, USART, SPI, I2C, USB interfaces.

---
Boards set for Raspberry Pi extension.
Python and Pawn scripts examples side by side.
New embedded script flashing dialog.

---
Scalable controller for pneumatic mechanism.
- The goal was to design cheap controller for a few mechanisms driven by pneumatic valves and electric motors.
- Minimize parts cost and PCB tooling cost.
- Number of controllers was small.
- Number of elements to control was not fixed and was relatively large ~150-200.

---
Scalable controller for pneumatic mechanism.
Taking into account all possible combinations of pneumatic actuators, motors and sensors in all mechanism configurations
- it turned out that “optimal” numbers of different PCB types was 2.
- Boards are interconnected by power lines, common I2C bus and 2 digital lines for synchronous triggering.
- External communication was performed by either I2C or USB by single board computer running Linux OS.
- During debugging stage also was equipped by embedded Pawn machine for easy movement algorithms trying/implementing.

---
USB powered expandable motor controller
- The same approach applied to motor control application.
- PCB with integrated USB driven power supply.
- One board can drive 2 stepper motors, 1 DC motor, 2 sensors.
- Scalable design by reusing the same board a few times and addressing individual boards using I2C bus and GPIO triggering for synchronization.

---
3rd party bipotentiostat control module.
- 2 analog outputs +/-10V
- 4 analog inputs +/-10V
- External digital trigger
- One switchable analog output
- Analog precision to achieve 1mV
- USB computer interface
- Spend minimum resources as client had no extra money to finance the development.

---
3rd party bipotentiostat control module.
- Mostly used 5% or 1% resistors
- Built in mcp3063 based boost 5V to 12V and inverting 5V to -12V switching sources.
- On board temperature sensor for calibration purposes.
Calibration setup was equipped with potentiometers and a heater under near the device for statistical data acquisition

---
3rd party bipotentiostat control module.
- Input filter design and Bode plot.
- Based on Chebyshev filter but with lowered response near cutoff requency to reduce oscillations caused by step response.

---
3rd party bipotentiostat control module.
Examples of parameters and outputs cross correlations
- After gaining statistical data went to higher dimensional space by involving first few powers of each parameter, exponentiation and a few parameter products.
- Used this data set to find the best mean out of sample error by applying linear regression to all possible parameter combinations.
- Obtained formulas and dropped parameters which didn't improve match better then chosen margin ( )
1^{-5}

---
3rd party bipotentiostat control module.
Formulas obtained for data readings conversion
V_{out} = a_{1} * dac_{1} + a_{2} * dac_{2} + a_{3} * dac_{1} * T + a_{4} * dac_{ 2 } * T + a_{5}*T^{3} + a_{ 6 }
V_{i n} = a_{1} * adc + a_{2} * T + a_{3} * T^{2} + a_{4} * T^{3} + a_{5}

---
3rd party bipotentiostat control module.
PC based software for driving control module.
Just nice looking electrochemical cycling I(V) curve obtained during system testing.